## Slide 1: Chapter 5 Analog Transmission
School of Computer Science and Engineering
Pusan National University
Jeong Goo Kim

## Slide 2: Homework
    Homework
Solve problems
  P5-1 What is the required bandwidth for the following cases if we need to send 6000 bps? Let d=1
    a. ASK
    b. FSK with 2Δf=4 KHz
    c. QPSK
    d. 16-QAM
  P5-6 Draw the constellation diagram for the following:
    a. ASK, with peak amplitude values of 1 and 3
    b. BPSK, with a peak amplitude value of 2
    c. QPSK, with a peak amplitude value of 3
    d. 8-QAM with two different amplitude values, 1 and 3, and four different phases

## Slide 3: Homework
  P5-7 Calculate the baud rate for the given bit rate and type of modulation
    a. 3000 bps, FSK
    b. 2000 bps, ASK
    c. 4000 bps, QPSK
    d. 36,000 bps, 64-QAM
  P5-12 The telephone line has 4 KHz bandwidth. What is the maximum number of bit we can send using each of the following techniques? Let d=0.
    a. ASK b. QPSK c. 16-QAM d. 64-QAM
Read textbook pp. 155-181
Next Lecture
Chapter 6. Bandwidth Utilization: Multiplexing and Spectrum Spreading