## Slide 1: Homework Chapter 6 Bandwidth Utilazation
School of Computer Science and Engineering
Pusan National University
Jeong Goo Kim

## Slide 2: Homework
    Homework
Solve problems
  P6-1 We need to use synchronous TDM and combine 20 digital sources, each of 200 Kbps. Each output slot carries 2 bit from each digital source, but one extra bit is added to each frame for synchronization. Answer the following questions.
    a. What is the size of an output frame in bits?
    b. What is the output frame rate?
    c. What is the duration of an output frame?
    d. What is the output data rate?
    e. What is the efficiency of the system(ratio of useful bits to the total bits)?
  P6-14 Answer the following questions about a T-1 lines.
    a. What is the duration of a frame?
    b. What is the overhead(number of extra bits per second)?
  P6-16 We need to transmit 100 digitized voice channels using a passband channel of 30 KHz. What should be the ratio of bits/Hz if we use no guard band?