## Slide 1: Chapter 4 Digital Transmission
School of Computer Science and Engineering
Pusan National University
Jeong Goo Kim

## Slide 2: Ch. 4 Outline
    Outline
4.1 Digital-to-Digital Conversion
4.2 Analog-to-digital
4.3 Transmission Modes

## Slide 3: Ch. 4 Objective
    Objective
Digital-to-digital conversion.
  Line coding
  block coding (redundancy)
  scrambling
Analog-to-digital conversion
  Pulse code modulation
  Delta modulation
Transmission modes
  serial transmission
  parallel transmission

## Slide 4: 4.1 Digital-to-Digital Conversion
    4.1 Digital-to-Digital Conversion
    4.1.1 Line Coding
is the process of converting digital data to digital signals
Fig. 4.1 Line coding and decoding

## Slide 5: 4.1 Digital-to-Digital Conversion
    Characteristics
Signal element vs. Data element
Fig. 4.2 Signal elements versus data elements

## Slide 6: 4.1 Digital-to-Digital Conversion
Data rate vs. Signal rate
  Data rate : bit rate
  Signal rate : pulse rate, modulation rate, or baud rate
Here N is data rate and r is the number of data elements carried by each signal element
  Average signal rate Savg = c × N × (1/r) baud, here c is the case factor
Ex. 4.1

## Slide 7: 4.1 Digital-to-Digital Conversion
Bandwidth
  effective bandwidth is finite
  minimum bandwidth Bmin = c × N × (1/r)
  maximum data rate Nmax = (1/c) × B × r
Ex. 4.2
Baseline Wandering
DC component
Self-synchronization
Built in error detection
Immunity to Noise and Interference
Complexity

## Slide 8: 4.1 Digital-to-Digital Conversion
Ex. 4.2
Fig. 4.3 Effect of lack of synchronization

## Slide 9: 4.1 Digital-to-Digital Conversion
    4.1.2 Line Coding Schemes
Fig. 4.4 Line coding scheme

## Slide 10: 4.1 Digital-to-Digital Conversion
    Unipolar Schemes
All the signal levels are on one side of the time axis
NRZ(Non-Return-to-Zero)
Fig. 4.5 Unipolar NRZ scheme

## Slide 11: 4.1 Digital-to-Digital Conversion
    Polar Schemes
All the signal levels are on both side of the time axis
NRZ-L(NRZ-Level), NRZ-I(NRZ-Inversion)
  average signal rate is N/2 Bd.
  DC component and self-synchronization problem
Fig. 4.6 Polar NRZ-L and NRZ-I
Ex. 4.4 Savg=N/2=500 kbaud, Bmin= S = 500 kHz

## Slide 12: 4.1 Digital-to-Digital Conversion
    Polar Schemes
RZ(Return-to-Zero)
  Self-synchronization
  Large bandwidth
Fig. 4.7 Polar RZ

## Slide 13: 4.1 Digital-to-Digital Conversion
    Polar Schemes
Biphase: Manchester and Differential Manchester
  Self-synchronization
  No DC component
  Large bandwidth
Fig. 4.8 Polar Biphase: Manchester and Differential Manchester

## Slide 14: 4.1 Digital-to-Digital Conversion
    Bipolar Schemes
Use three levels, positive, zero, and negative
Alternate Mark Inversion(AMI), pseudoternary
  No DC component
    Fig. 4.9 Bipolar Schemes: AMI, pseudoternary

## Slide 15: 4.1 Digital-to-Digital Conversion
    Multilevel Schemes
mBnL: m-bit n-level
2B1Q(2-bit 1-quaternary)
    Fig. 4.10 Multilevel: 2B1Q

## Slide 16: 4.1 Digital-to-Digital Conversion
    Multilevel Schemes
8B6T(8-bit 6-ternary)
  100BASE-4T
  28(256) < 36(729)
    Fig. 4.11 Multilevel: 8B6T

## Slide 17: 4.1 Digital-to-Digital Conversion
    Multilevel Schemes
4D-PAM5(4-dimensional 5-level pulse amplitude modulation)
    Fig. 4.12 Multilevel: 4D-PAM5

## Slide 18: 4.1 Digital-to-Digital Conversion
    Multitransition: MLT3
    Fig. 4.13 Multitransition: MLT3

## Slide 19: 4.1 Digital-to-Digital Conversion
    Summary of Line Coding Schemes
    Table 4.1 Summary of Line Coding Schemes

## Slide 20: 4.1 Digital-to-Digital Conversion
    4.1.3 Block Coding
  mB/nB - (n-m) redundancy
  to ensure synchronization
  for error control
Fig. 4.14 Block coding concept

## Slide 21: 4.1 Digital-to-Digital Conversion
    4B/5B
  NRZ-I + synchronization
Fig. 4.15 Using block coding 4B/5B with NRZ-I line coding scheme

## Slide 22: 4.1 Digital-to-Digital Conversion
    Table 4.2 4B/5B mapping codes

## Slide 23: 4.1 Digital-to-Digital Conversion
Fig. 4.15 Substitution in 4B/5B block coding
Ex. 4.5

## Slide 24: 4.1 Digital-to-Digital Conversion
    8B/10B
  5B/6B + 3B/4B
Fig. 4.17 8B/10B block encoding

## Slide 25: 4.1 Digital-to-Digital Conversion
    4.1.4 Scrambling
Substitutes long zero-level pulses with a combination of other levels to provide synchronization
Fig. 4.18 AMI used with scrambling

## Slide 26: 4.1 Digital-to-Digital Conversion
B8ZS(Bipolar with 8 zero substitution)
Fig. 4.19 Two cases of B8ZS scrambling technique

## Slide 27: 4.1 Digital-to-Digital Conversion
HDB3(High-density bipolar 3-zero)
Fig. 4.20 Different situations in HDB3 scrambling technique

## Slide 28: 4.2 Analog-to-Digital Conversion
    4.2 Analog-to-Digital Conversion
    4.2.1 Pulse Code Modulation (PCM)
The most common technique to change an analog signal to digital data (digitization)
Fig. 4.21 Components of PCM encoder

## Slide 29: 4.2 Analog-to-Digital Conversion
    Sampling
  Ideal Sampling
  Natural Sampling
  Flat-top Sampling (sample and hold)
Fig. 4.22 Three different sampling methods for PCM

## Slide 30: 4.2 Analog-to-Digital Conversion
    Sampling rate
  Nyquist theorem : the sampling rate must be at least 2 times the highest frequency contained in the signal
Ex. 4.6
Ex. 4.7
Fig. 4.23 Nyquist sampling rate for low-pass and bandpass signals

## Slide 31: 4.2 Analog-to-Digital Conversion
Fig. 4.24 Recovery of a sine wave with different sampling rates.

## Slide 32: 4.2 Analog-to-Digital Conversion
Fig. 4.25 Sampling of clock with only one hand.

## Slide 33: 4.2 Analog-to-Digital Conversion
    Quantization
  The process of converting a discrete-time continuous-amplitude signal into a digital signal by expressing each sample value as a finite number of digits, is called quantization
Fig. 4.26 Quantization and encoding of a sampled signal

## Slide 34: 4.2 Analog-to-Digital Conversion
Quantization error
  The error introduced in presenting the continuous-valued signal by a finite set of discrete value level is called quantization error or noise
  Quantization Levels L=2n (n-bit quantization)
  Step size Δ=(Vmax – Vmin)/L
Signal to Quantization Noise Ratio (SNQR)
  Assumptions: Linear quantization, zero mean signal, uniform pdf. uniform quantization
SNRdB = 6.02n dB
  Assumptions: Linear quantization, sinusoidal signal, uniform quantization
SNRdB = 6.02n + 1.76dB

## Slide 35: 4.2 Analog-to-Digital Conversion
Companded PCM (non-uniform quantization)
  Linear quantization: suitable for the information signal has a uniform pdf.
  Nonlinear quantization: companding (compressing-expanding)
Fig. Compression and expanding

## Slide 36: 4.2 Analog-to-Digital Conversion
μ-law and A-law
  μ = 255 in the USA & Canada ⇒ 24dB quantization noise reduction
Fig. μ-law and A-law

## Slide 37: 4.2 Analog-to-Digital Conversion
    Encoding
  Bit rate = sampling rate × number of bits per sample = fs × nb
Ex. 4.14
Original Signal Recovery
Fig. 4.27 Components of a PCM decoder

## Slide 38: 4.2 Analog-to-Digital Conversion
    PCM Bandwidth
  Bmin = c × N× 1/r = c × nb × fs × 1/r = c × nb × 2 × Banalog × 1/r
  for r = 1, c = 1/2
  Bmin = nb × Banalog
Ex. 4.15
Maximum Data Rate of a Channel
  Nmax = 2 × B× log2L bps
Minimum required Bandwidth
  Bmin = N / (2 × log2L) Hz

## Slide 39: 4.2 Analog-to-Digital Conversion
    4.2.2 Delta Modulation (DM)
Transmit information about the changes between samples instead of sending the sample values themselves.
Fig. 4.28 The process of delta modulation

## Slide 40: 4.2 Analog-to-Digital Conversion
Fig. 4.29 Delta modulation components
Fig. 4.30 Delta demodulation components

## Slide 41: 4.3 Transmission Modes
    4.3 Transmission Modes
Fig. 4.31 Data Transmission Modes

## Slide 42: 4.3 Transmission Modes
    4.3.1 Parallel Transmission
    Fig. 4.32 Parallel Transmission

## Slide 43: 4.3 Transmission Modes
    4.3.3 Asynchronous Transmission
    Fig. 4.34 Asynchronous Transmission

## Slide 44: 4.3 Transmission Modes
    4.3.4 Synchronous Transmission
    Fig. 4.35 Synchronous Transmission

## Slide 45: Homework
Homework
Read textbook pp. 135-150
Next Lecture
Chapter 5. Analog Transmission